This program is a scaled down version of spice that will
simulate and find the frequency response
of any circuit.  It has no time domain simulation
capabilities.  sspice can accept passive and active
circuits.   Voltage controlled current sources and
voltage controlled voltage sources are available.

Node Names

The input format of sspice is a "net list" containing
all component connections and values.  Most components
are described as to be connected between two nodes.
The node names can be a 10 or less ascii character
string.  The node names "Gnd" and "gnd" are reserved
for the common node of ground.  Each circuit is assumed
to have this common node of ground.

Control Commands

FS <val> [modif] ;			The starting frequency in Hz.
FE <val> [modif] ;			The ending frequency in Hz.
FP <val> [modif] ;			The number of partitions the
					frequency range is to divided
					into.
LOG ;					The output will be calculated in
					dB (attenuation).  Only applies
					to magnitude response.
RADS ;					The starting, ending, and output
					printed frequencies are accepted
					and printed in radians instead of Hz.
PHASE ;					Phase response is calculated and
					printed in degrees.
PRTCMP ;				Print out a list of the components
					used and their node assignments.
OUT <node> ;				Identifies the output node.
VS <node> ;				Identifies the input node.

Passive Component Entries

Rxxxx <node> <node> <value> [modif] ;	A resistor with label "xxxx" connected
					between the two nodes with resistance
					"value" ohms.
Cxxxx <node> <node> <value> [modif] ;	A capacitor with label "xxxx" connected
					between the two nodes with capacitance
					"value" farads.
Lxxxx <node> <node> <value> [modif] ;	An inductor with label "xxxx" connected
					between the two nodes with inductance
					"value" henries.

Active component Entries

VCV <node1> <node2> <node3> <value> [modif] ;
					A voltage controlled voltage source.
					A voltage of value*(Vnode1-Vnode2)
					is applied to node3.  "value" is the
					voltage gain constant (for typical
					op-amps, make this 100,000).
VCI <node1> <node2> <node3> <node4> <value> [modif] ;
					A voltage controlled current source.
					A current of value*(Vnode1-Vnode2)
					is injected between node3 and node4.
					"value" is considered to be the
					transconductance of the controlled
					source in units of Mhos.

Note: At present, sources cannot be assigned unique names; however,
      each entry is considered a unique source.

Modifiers

All input data can be modified by a metric modifier or an exponential power.
The modifiers are p,n,u,m,K,M,G, for ten to the -12,-9,-6,-3,+3,+6,+9
powers, respectively.

Output

The output will be two columns of numbers: the first being the
frequency in hertz, the second being the amplitude response
in absolute units or attenuation in dB, phase response in
degrees, or the step response.  In addition to the x-y
coordinates, further information is supplied to the
output for use by the "plot" program.