!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!HELP FOR MOVE!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!

This is a sample file for 'move'. Set your own input and output files.  Input
file must be mono, and output must be a stereo (2-channel) file.
********************************************************************************
input ("sf/infile")
output ("sf/outfile")

space (dist_to_front, dist_to_right, -dist_to_back, -dist_to_left, height,
       abs_fact, rvbtime)

path(time0,distance0,angle0, time1,distance1,angle1, ..., timeN,distN,angleN)

			-------- or --------

cpath(time0,xcoord0,ycoord0, time1,xcoord1,ycoord1, ..., timeN,xcoordN,ycoordN)

threshold(reset_distance)

move (inskip, outskip, dur, amp, dist_between_mikes, rvb_amp)

********************************************************************************

space is the setup call for the room in which the sound will appear.  Since the
listener (YOU) is at point (0,0) coordinate-wise, the locations of the 4 walls
are specified like in an x,y coordinate system:

                                  y
                                  |
                             -x---0---x
                                  |
                                 -y

Therefor the distance to the back and left walls must be specified as negative.
All, including height, are in feet. Abs_fac is a number between 0 (min) and
10 (max) that determines how reflective the walls are.  Rvbtime is the approx-
imate length of reverb in seconds (max depends on roomsize). 

********************************************************************************
Path allows you to specify the trajectory of the sound source as triplets
representing relative time (as in setline), distance (in feet), and angle (in
degrees).

                                  0.0    source
                                   |    /
                                   |   /
                                   |  /
                                   | /
                                   |/
                                  you

Be sure to stay inside bounds of the room (it may take a bit of trigonometry 
[or guessing] to do that).

If you prefer cartesian coordinates, use cpath instead, entering triplets of
time, x coordinate (left-right), y coordinate (front-back).

	                                         source
       		                            	 |     
               		                    	 |     
                       		            	 |     
                     		              	 |    
                    		              	 | (y dist.)  
                   		               	 |  
                  	              (x dist.)	 | 
                       		 you-------------


********************************************************************************
Threshold allows you to determine how often the program updates the location
of the source.  A typical value is 0.01 (feet). Smaller values give somewhat
smoother results at the cost of run time (which can go as high as 600 to 1!!).

********************************************************************************
Move has its first 3 args the same as mix, etc.

amp: amplitude factor for input signal (done before any of the processing).

dist_between_mikes: remember that this simulates a stereo image.  Your 'mikes'
should be anywhere from 1 to, say, 10 feet apart depending on the size of the
room.

The last number is a global amp factor that affects all reflections and reverb
equally, but not the direct signal.  This is usually set to 1.0.

********************************************************************************
Have fun, and remember that it runs at about 125 to 1 right now, faster or
slower depending on the motion and threshold resolution.

Doug Scott